## Slide 1: AVA-SH Test Review
Team f5
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 2
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
Notes: Windows/Linux PC:
-will be acting as server, using a MainServer class, the DSKY interface and custom made datatypes
-able to communicate with all modules using UDP
Media Controller
-used to play music, and possibly video
-Has database of music and video the user can play
Light Controller:
-RPi will communicate with 1 component
1. LED’s: used to slowly brighten room
-will be controlled using PWM on a GPIO pin
-also has a speaker used to play an alarm (using the 3.5mm jack on the RPi)
Coffee Maker:
-RPi will communicate with 3 components:
1. Electronic Scale: used to weigh cup before and during coffee making to make sure proper amounts of coffee are made
-interfaced using USB port on RPi
2. Thermometer: used to monitor water temp
-interfaced using AD converted on Gertboard
3. Heating Element: used to heat water
-interfaced via RPi GPIO connected to a simple transistor
Terminal:
-GUI for user to enter commands to AVA

## Slide 3
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
User Interfaces
Voice Interface
Terminal on RPi
Android App
Modules
Smart Coffee Machine
Smart TV/Sound-System
Alarm
Central AVA Server
Notes: Network Diagram of the AVA-SH
The user interfaces do not communicate directly with the modules, they only communicate with the server which can then pass the commands to the modules
The modules also should not communicate directly with each other, to maintain high modularity
Uses Client-Server design, wherein the modules/interfaces are the clients and the server is the main AVA serve

## Slide 4: Unit Testing: General Utility Class
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
DataChannel.java
Notes: -Automatically packs and unpacks packets
-Ease of formatting
-Used globally throughout the system
-UDP packets
For all tests we use TWO instances of DataChannel
One for sending+packing packets
One for receiving+unpacking packets

## Slide 5: testUnpackBadPacket
  Description:
  Creates a non-valid packet with
    Type: 0xAD
  DataChannel detects the invalid opcode during packet unpacking
  Results in a thrown NetworkException
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
Notes: Document on packet types and uses @  https://github.com/SYSC-3010-F5/AVA-SH/blob/master/docs/Packet-Format.txt
Packet send with invalid opcode
Receiving DataChannel

## Slide 6: testUnpackCommand1
  Description:
  Creates a command packet with
    Command Key: “new alarm”
    Extra Info: “{hour: 7, minute: 00, name: wake_up}”
  DataChannel assembles and sends the command packet
  DataChannel receives the packet and unpacks
  Received data should have identical Type, Command Key and Info
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
Notes: -Command packets contain two fields
-Command Key
-Extra Info
-These fields change for each type of command we wish to send
-The sender inputs the parameters, Command Key and Extra Info

## Slide 7: testUnpackCommand2
  Description:
  Creates a command packet with
    Command Key: “toggle light”
    Extra Info: “”
  DataChannel assembles and sends the command packet
  DataChannel receives the packet and unpacks
  Received data should have identical Type, Command Key and Info
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 8: testUnpackError1
  Description:
  Creates an error packet with
    Error Message: “you’ve broken something”
  DataChannel receives the packet and unpacks
  Received data should have identical Type and Error Message
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 9: testUnpackError2
  Description:
  Creates an error packet with
    Error Message: “”
  DataChannel receives the packet and unpacks
  Received data should have identical Type and Error Message
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 10: testUnpackInfo1
  Description:
  Creates an info packet with
    Info Message: “some info goes here”
  DataChannel receives the packet and unpacks
  Received data should have identical Type and Error Message
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 11: testUnpackInfo2
  Description:
  Creates an info packet with
    Info Message: “”
  DataChannel receives the packet and unpacks
  Received data should have identical Type and Error Message
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 12: testHandshake1
  Description:
  Creates a handshake packet with Type 0x00
    Handshake Key: “Handshake Test”
    Device name: “Terminal”
  DataChannel receives the packet and unpacks
  Received data should have identical Key and Device
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 13: testHandshake2
  Description:
  Creates a handshake packet with Type 0x00
    Handshake Key: “”
    Device name: “”
  DataChannel receives the packet and unpacks
  Received data should have identical Key and Device
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 14
No. | Title | Context | Inputs | Expected Outputs
1 | testUnpackBadPacket | PacketWrapper, DataException | Type: 0xAD | Network Exception
2 | testUnpackCommand1 | PacketWrapper, DataException | Command Key: “new alarm” Extra Info: “{hour: 7, minute: 00, name: wake_up}” | Identical Type, Command Key and Info
3 | testUnpackCommand2 | PacketWrapper, DataException | Command Key: “toggle light” Extra Info: “” | Identical Type, Command Key and Info
4 | testUnpackError1 | PacketWrapper, DataException | Error Message: “you’ve broken something” | Identical Type and Error Message
5 | testUnpackError2 | PacketWrapper, DataException | Error Message: “” | Identical Type and Error Message
6 | testUnpackInfo1 | PacketWrapper, DataException | Info Message: “some info goes here” | Identical Type and Info Message
7 | testUnpackInfo2 | PacketWrapper, DataException | Info Message: “” | Identical Type and Info Message
8 | testHandshake1 | PacketWrapper, DataException | Handshake Key: “Handshake Test” Device name: “Terminal” | Identical Type, Handshake Key and Device Name
9 | testHandshake2 | PacketWrapper, DataException | Handshake Key: “” Device name: “l” | Identical Type, Handshake Key and Device Name
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 15: Temperature Sensor Stub
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 16: testCoffeeEvent
  Description:
  Sends a command to make coffee at a specified time in the future
    Command Key: “sch event”
    Extra info: JSON formatted text containing trigger time and command
  DataChannel receives the packet and unpacks
  CoffeeController parses the JSON and sets a ServerEvent at the trigger time
  Once the trigger time is reached, turn on the coffee machine and begin polling the temperature sensor
  Temperature sensor should return higher and higher temps
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 17: testPeriodicCoffee1
  Description:
  Schedules coffee to be made repeatedly
    Command Key: “sch event”
    Extra info: JSON file, with trigger times as 7 AM every day
  DataChannel receives the packet and unpacks
  CoffeeController creates the ServerEvent
  CoffeeController turns on coffee machine at 7 AM
  CoffeeController turns on coffee machine again at 7 AM the next day
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 18: testPeriodicCoffee2
  Description:
  Schedules coffee to be made repeatedly
    Command Key: “sch event”
    Extra info: JSON file, with trigger times as 7 AM every Wednesday and Friday
  DataChannel receives the packet and unpacks
  CoffeeController creates the ServerEvent
  CoffeeController turns on coffee machine at 7 AM, Wednesday
  CoffeeController turns on coffee machine again at 7 AM the next Friday
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 19: Unit Testing: Embedded Unit Test
No. | Title | Context | Inputs | Expected Outputs
1 | testCoffeeEvent | CoffeeController, DataChannel | Command Key: “sch event” Extra Info: JSON file | Temp. sensor heats up at trigger time
2 | testPeriodicCoffee1 | CoffeeController, DataChannel | Command Key: “sch event” Extra Info: JSON file | Temp. sensor heats up at trigger times
3 | testPeriodicCoffee2 | CoffeeController, DataChannel | Command Key: “sch event” Extra Info: JSON file | Temp. sensor heats up at trigger times
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 20: Unit Testing: Distributed System Unit Test
No. | Title | Inputs | Expected Outputs
1 | testPing | Command packet with key: “ping” | Empty info packet
2 | testSchEvent | Command packet with key: “sch event”, extra info describing event parameters | Empty info packet, event triggering at set time
3 | testSetTimer | Command packet with key: “set timer”, extra info describing timer parameters | Empty info packet, timer sounding after set time
4 | testNewAlarm | Command packet with key: “new alarm”, extra info describing alarm parameters | Empty info packet, alarm sounding at set time
5 | testReqTime | Command packet with key: “time” | Info packet with time
6 | testReqIp | Command packet with key: “req ip”, extra info: “<STR>” | Info packet with IP of module registered under <STR>
7 | testNp-Events | Command packet with key: “req np-events” | Info packet with all non-periodic events (like timers)
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
Notes: no star denotes packet from an interface to server
* denotes packet from server to alarm
** denotes packet from server to coffee maker
*** denotes packet from coffee maker to server
What we got so far, will be increased.
Due to the high degree of modularity in the system, this list will change. Wee keep an updated list on our git. It describes all commands, parameters and expected outputs.
Empty info pack=succesfull

## Slide 21: Unit Testing: Distributed System Unit Test
No. | Title | Inputs | Expected Outputs
8 | testReqP-Events | Command packet with key: “p-events” | Info packet with all periodic events (like alarms)
9 | testDelNp-Events | Command packet with key: “del np-event”, extra info: “<STR>” | Empty info packet, non-periodic event with name <STR> removed from scheduling (will not trigger)
10* | testLedOn | Command packet with key: “led on” | RPi-Alarm LED turns on
11* | testLedOff | Command packet with key: “led off” | RPi-Alarm LED turns off
12* | testLEDPWM | Command packet with key: “led pwm”, extra info: seconds until max | Alarm LED PWM starts, LED starts at minimum brightness, takes x seconds to reach maximum brightness
13* | testAlarmOn | Command packet with key: “alarm on” | RPi-Alarm plays alarm tone on speaker
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
Notes: no star denotes packet from an interface to server
* denotes packet from server to alarm
** denotes packet from server to coffee maker
*** denotes packet from coffee maker to server

## Slide 22: Unit Testing: Distributed System Unit Test
No. | Title | Inputs | Expected Outputs
14* | testAlarmOff | Command packet with key: “alarm off” | RPi-Alarm stops alarm tone from being played on speaker
15** | testCoffeeOn | Command packet with key: “coffee on” | Coffee Machine turns on
16** | testCoffeeOff | Command packet with key: “coffee off” | Coffee Machine turns off
17*** | testCoffeeReady | Info packet with info: “coffee ready” | Push notification on App / Dialog print on Terminal
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
Notes: Commands can be seen @  https://github.com/SYSC-3010-F5/AVA-SH/blob/master/docs/AVA-Command-Manifest.txt
no star denotes packet from an interface to server
* denotes packet from server to alarm
** denotes packet from server to coffee maker
*** denotes packet from coffee maker to server

## Slide 23: Acceptance Testing & Distributed System Scenarios
  System Requirements:
  Allow the user to schedule multiple system actions to occur at a certain time
  Respond to user commands from both a mobile app and computer terminal in a timely manner
  The system should be highly modular
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
Notes: The system will need to be able to execute certain actions at pre-defined times, such as brightening the wake-up lamp a certain time before wake-up
The system will need to answer and execute user commands quickly, with little perceived delay
The system should be highly modular, to make adding new modules easy, as well as encourage the use of modules

## Slide 24: Setting an alarm
  User selects “New Alarm” Button App-side
  Command packet sent to the server with
    Command Key: “new alarm”
    Extra Info: “{hour: 7, minute: 00, name: wake_up}”
  Server interprets the command and sets a “Server Event Timer”
  Event expires and a packet is sent to the alarm RPi with
    Command Key: “alarm on”
    Extra Info: “”
  Alarm blares
  Alarm can be silenced by any button on the RPi
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 25: Start Coffee Maker
  User selects “Start Coffee” Button App-side
  Command packet sent to the server with
    Command Key: “coffee on”
    Extra Info: “”
  Server interprets the command and sends a “Start” packet to the dedicated coffee based RPi
  Coffee is started and completed when the Scale prompts the RPi
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 26: Create a wake alarm
  User selects “Wake Alarm” Button App-side
  Command packet sent to the server with
    Command Key: “wake alarm”
    Extra Info: “{hour: 7, minute: 00, pwm: 60(seconds) name: wake_alarm}”
  Server creates two “Scheduled Events”
  One to send the alarm RPi a packet with
    Command Key: “led pwm”
    Extra Info: “{time: 60(seconds)}”
  The LED wake light starts to brighten
  Once fully lit another packet is sent to the alarm RPi with
    Command Key: “alarm on”
    Extra Info: “”
  Alarm can be silenced by any button on the RPi
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven

## Slide 27
SYSC 3010 Cheung, Charlebois, Garlough, Van Kerkhoven
Milestone Name | Scheduled Completion Date | Actual Completion Data
Basic Server Framework | February 12th | February 21st
Terminal Functionality | February 19th | February 10th
Communication Protocol Finalized + Implemented | February 26th | February 20th
Testing Server-Terminal Communication on separate machines | February 28th | February 26th
Scheduling Timed Events | March 4th | March 3rd
App Functionality | March 4th | March 2nd
Full System Test with at least one module | March 12th | N/A
Notes: -Both Terminal and Server complete
-App has a framework, without any backend implementation
-Hardware has been ordered and most has arrived
-integration of arrived sensors in underway